## Slide 1: Runtime Programmable Switches
Jiarong Xing, Kuo-Feng Hsu, Matty Kadosh, Alan Lo, Yonatan Piasetzky, Arvind Krishnamurthy, Ang Chen

## Slide 2
p4c compiler
P4 switch
Background: Programmable switches
Switches become fixed after the program is deployed.
Operators compile and reflash the data plane w/ a new program
However, reflashing can cause downtime and packet loss
To avoid downtime, traffic drain/undrain is necessary
  Changes must be infrequent and operator driven
p4c compiler
P4 switch
P4 switch
“Fixed” function
Routing
Telemetry
Security
…

## Slide 3
From compile-time to runtime programmability
The key features of runtime programmability:
  Runtime: Live upgrade at runtime
  Seamless: Zero downtime and packet loss
  Partial: Upgrade the program partially
  Atomic: Reprogram with strong consistency guarantees
Runtime reconfiguration
Runtime programmable switch
Program updates

## Slide 4
Benefits of runtime programmability
Example benefits of runtime programmability
  Real-time attack mitigation
  Just-in-time network optimization
  Tenant-specific network extension
Real-time attack mitigation
JIT optimization
Performance monitoring
Dynamic optimization
Tenant-specific extension

## Slide 5
FlexCore: A whole-stack design
current.p4
new.p4
FlexCore
An ecosystem that supports live program upgrades with strong consistency and no downtime.
Switch hardware
Switch hardware design
Partial reconfig primitives
Atomic changes
Multi-level consistency
The FlexCore ecosystem
delta

## Slide 6
Challenge #1: Flexible switch architecture
The RMT architecture is inflexible for runtime changes
  Compute and memory are tightly coupled in stages.
  Packets can only move forward to the next stage.
  Memory of one stage cannot be used by other stages.
Match
Action
Memory
Stage 1
pkt
pkt
Match
Action
Stage 2
pkt
pkt
Match
Action
Stage n
pkt
pkt
…

## Slide 7
Solution: Disaggregated RMT architecture
Enhanced disaggregated RMT (dRMT) architecture
  Compute and memory are disaggregated
  Memory is sharded, and accesses are load-balanced
  MA processors handle packets in parallel in a run-to-completion manner
Match
Action
…
PDTab
…
MA processor1
Load-balanced crossbar
Disaggregated, sharded access
Memory bank 1
Memory bank t
Match
Action
PDTab
Match
Action
PDTab
MA processor2
MA processorN

## Slide 8
Partial reconfiguration with indirection
FlexCore adopts a pointer-based indirection mechanism
Program description table (PDTab)
  Each PDTab entry records the information of a MA table
  PDTab entries are chained together by “next table pointers”
  Pointers can be changed at runtime atomically.
。。。
…
Memory banks
Match key
Key type
Mem pointer
Next table pointer
ipv4
route
Start
…
parser {
...
}
control ingress{
ipv4.apply();
+ acl.apply();
route.apply();
}
acl
Program description table (PDTab)
P4 program
①
②
③
④

## Slide 9
More partial reconfiguration primitives
AllocTab(T)
SetPtr(T, T’)
ModTab(T, T’)
if (condition) { tab.apply();
}
Match
Action
PDTab
AllocCond(B, Pred, Br1, Br2)
DeallocCond(B)
SetCondPtr(B, N1, N2)
AllocState(S)
AllocTrans(S1, S2)
AllocEx(R)
FlexCore provides a set of atomic reconfiguration primitives
FlexCore transforms program diff into these primitives
* Each allocation primitive has its respective deallocation primitive

## Slide 10
Challenge #2: Atomic changes
A program-level update may involve multiple discrete changes
Non-atomic changes lead to undesired intermediate states
A
B
E
s
C
F
r
D
A program-level update
x
New node
New edge
x
Pointer change
A
B
E
s
C
r
D
Undesired intermediate states
x
Reused node

## Slide 11
Solution: Version control with FlexEdge
FlexEdge: A version control mechanism
  Check on a global version metadata
  Can be inserted/deleted one by one atomically
i
FlexEdge
Current version
New version
Check on version number
A
B
E
s
C
F
r
D
i
i
i
1
0
1
1
0
0
Control with FlexEdge
A
B
s
C
r
D
i
i
i
Current version
A
B
E
s
C
F
r
D
i
i
i
New version
0
1

## Slide 12
Challenge #3: Finer-grained partial updates
One tx still requires preparing all the differences together
Could fail if the switch has insufficient headroom
First completed can release resources for later updates
We need multi-step transactions
A
B
D
C
E
r
A P4 program with two independent branches
Headroom
Peak transient overhead
Failure
Headroom
Peak transient overhead
Success
Do this first, it will release resources from table D
A
B
D
C
E
r
To delete
To add
Released by D

## Slide 13
Solution: Multi-level consistency for multi-step TXs
FlexCore supports multi-level consistency
Definitions and algorithms are in the paper!
B
E
s
C
F
D
Program consistency
B
E
s
D
s
C
F
Element consistency
B
E
s
s
C
F
E
s
D
Execution consistency
Weaker consistency, lower transient overhead
Tx 1
Tx 1
Tx 2
Tx 1
Tx 2
Tx 3

## Slide 14
Implementation and setup
Commercial switch hardware
  NVIDIA/Mellanox Spectrum-2 silicon
  As fast as 12.8Tbps
BMv2 emulator
  Reconfiguration primitives in P4Runtime
  Three consistency levels
  Available at https://github.com/jiarong0907/FlexCore
Case study setup
  Accelerated multicast
  A spectrum-2 switch connected with one sender and several subscribers
  The sender sends the same data to its subscribers

## Slide 15
Case study: Accelerated multicast
Runtime switch function upgrade with FlexCore has no downtime
Runtime network optimization greatly improves performance
Time
Unicast
Insert multicast
Remove multicast
Insert telemetry
Remove telemetry
Traffic throughput
Job completion time
Zero packet loss
20ns reduced

## Slide 16
More results in the paper
System overhead
Use cases
In-place application upgrade
Real-time attack mitigation
Tenant-specific network extensions
Multi-level consistency
Scalability of real-world P4 programs
Large-scale synthetic program simulation
Hardware overhead
Reconfiguration transient overhead

## Slide 17
Summary
Today’s switches are only programmable at compile time
FlexCore: An ecosystem for runtime programmability
  Live switch program upgrades
  Zero packet loss, no downtime
  Support partial upgrades with multi-level consistency guarantees
Implementation:
  12.8Tbps Spectrum-2 switch silicon
  BMv2 emulator: https://github.com/jiarong0907/FlexCore
Use cases:
  Runtime accelerated multicast, real-time attack mitigation, …
Ultimate vision:
  End-to-end runtime programmable networks
  See our vision paper at HotNets’21: A Vision for Runtime Programmable Networks